## Slide 1: Unit II :IO Port Interfacing-I

## Slide 2: Interfacing of 7 Segment display
Seven Segment Display
  7 segment LED display is very popular and it can display digits from 0 to 9 and quite a few characters (A,B,C.. etc)
  A seven segment display consists of seven LEDs arranged in the form of a squarish ‘8’ slightly inclined to the right and a single LED as the dot character.
  Different characters can be displayed by selectively glowing the required LED segments.
  Seven segment displays are of two types, common cathode and common anode

## Slide 3
In common cathode type , the cathode of all LEDs are tied together to a single terminal which is usually labeled as ‘com‘ and the anode of all LEDs are left alone as individual pins labeled as a, b, c, d, e, f, g & h (or dot) .
In common anode type, the anode of all LEDs are tied together as a single terminal and cathodes are left alone as individual pins.
Digit drive pattern of a seven segment LED display is simply the different logic combinations of its terminals ‘a’ to ‘h‘ in order to display different digits and characters.
The digit drive patterns (0 to 9) of a seven segment display is dependent on the way in which interfacing is done.

## Slide 4: algorithm
Start
Initialize DPTR
Initialize the counter
Clear Accumulator
Use MOVC instruction to access look up table* where the digit drive pattern is stored
Load the data on the port and call delay
Increment the pointer and decrement the counter
Loop
*Store the drive pattern using the directive DB (define byte).

## Slide 5: Interfacing of LCD with 8051
Advantages of using LCDs
The ability to display numbers, characters, and graphics. This is in contrast to LEDs, which are limited to numbers and few characters.
Clarity of the display
  On seven segment display; character ‘B’ and number ‘8’ are displayed in same fashion
Ease of programming
In corporation of a refreshing controller into the LCD, thereby reliving the CPU of the task of refreshing the LCD.

## Slide 6: LCD pin description
Pin number | Symbol | Level | I/O | Function
1 | Vss | - | - | Power supply (GND)
2 | Vcc | - | - | Power supply (+5V)
3 | Vee | - | - | Contrast adjust
4 | RS | 0/1 | I | 0 = Instruction input 1 = Data input
5 | R/W | 0/1 | I | 0 = Write to LCD module 1 = Read from LCD module
6 | E | 1, 1->0 | I | Enable signal
7-14 | DB0-DB7 |  |  | 
15 | VB+ | 1 | - | Backlight Supply
16 | VB- | 0 | - | 

## Slide 7: Commands for lcd
Command to LCD | Code (Hex)
Clear display screen | 01
Increment cursor (shift cursor to right) | 06
Display on cursor blinking | 0E
Force cursor to beginning of 1st line. | 80
Force cursor to beginning of 2nd line. | C0
2 lines and 5x7 matrixes. | 38

## Slide 8: Algorithm to interface lcd
Start
Initialize P2 and P1 where DB0 –DB7 and control lines(rs, rw, en) are interfaced respectively
Initialize LCD by sending appropriate commands (38h,0Eh,01h,06h,80h)
While sending commands; the control signals should be rs=0,rw=0,en= H-L
Load the data to be displayed on the data bus DB0 to DB7 and give appropriate control signals (rs=1, rw=0, en=H-L)
Give suitable delay wherever necessary.
Loop in order to send string.

## Slide 9: ADC interfacing
Basics:
Most of the signals are analog in nature.
    Temperature, humidity, pressure etc
The operations performed in an A to D Converter
    Sampling
    Quantification
    Coding
Parameters
  Resolution: n-bit ADC will have n bit resolution
  Higher the resolution smaller the step size.
  Conversion time: time taken to convert analog i/p into digital value
  Reference voltage: decides the maximum range

## Slide 10
Successive approximation ADC
ADC 0808 has 8 input channel and three select lines A,B,C and ALE to latch the address of i/p channel
Control/hand shaking signal: SOC,EOC and OE

## Slide 11: Algorithm
Start
Select an analog channel by providing suitable data to A B &C and activate the ALE signal (L-H)
Activate SOC(Start of conversion) L-H pulse to initiate the conversion
Monitor EOC(End of Conversion , H-L pulse) to see whether conversion is over and ready to be picked up
Activate OE(output enable ,L-H pulse) signal in order to read the digital data out of ADC chip
Display the result on LCD or LED bank

## Slide 12: Limitations Of 8 bit Microcontroller
Data bus width limits speed of execution
Addressable memory is limited for given application
Very small RAM & Flash memory
Does not have high performance interrupt system
Does not have DMA & cache memory for faster execution
Does not have memory protection unit MPU
Does not have protected modes of operation
Can not implement RTOS which is current need of embedded system